## Slide 1: Livestock Projects
TeamAg, Inc
120 Lake Street
Ephrata, PA 17522
717-721-6795
teamag@teamaginc.com
Planning & Permitting Process for a Proposed CAFO Operation

## Slide 2: TeamAg, Inc. – What we do…
Consulting – Manure Management Plans, Agriculture E&S Plans, Conservation Plans, Nutrient Management Plans, Odor Management Plans, CAFO Permitting, Other Permits, Field Mapping, Crop Scouting
Engineering – Construction E&S Plans, Site Planning, Storm Water Plans, NPDES Permits, Water Quality Permits, Designs & Certifications, Zoning Permitting, Site Surveying

## Slide 3: Manure Planning – What do livestock operations need?
DEP requires that all farms that generate or handle manure must have a plan that outlines the storage and handling of the manure
The type of plan needed depends on the farm’s regulatory status, non-CAO or non-CAFO vs. CAO or CAFO
Majority of farms with livestock are not a CAO or CAFO and therefore only need a manure management plan to meet DEP requirements
This plan can be completed by the farmer or a consultant
It is not reviewed or approved by DEP, but must be kept on the operation at all times and implemented by the farm

## Slide 4: CAO – What is it?
Created by the Pennsylvania Nutrient Management Law, Act 38. Administered by the PA SCC.
Only livestock operations with 2 or more AEUs (Animal Equivalent Units) per acre are affected by this law. They are called Concentrated Animal Operations – CAOs.
1 AEU = 1,000 pounds of live animal and all types of animals are counted.
Operations falling under this program must have a current nutrient management plan developed by a certified nutrient management specialist and be approved by the local county conservation district’s board of directors. The plan must address nitrogen and phosphorus.
There are also mechanical manure application set backs and restrictions that must be followed.

## Slide 5: Example CAO Calculation #1
Dairy Farm #1
300 Milk Cows at 1,300 lbs per cow
125 Heifers at 900 lbs per cow
50 Calves at 375 lbs per cow
300 * 1,300 / 1,000 = 390 AEUs
125 * 900 / 1,000 = 112.5 AEUs
50 * 375 / 1,000 = 18.75 AEUs
390 + 112.5 + 18.75 = 521.25 AEUs Total
521.25 AEUs / 1,100 acres = 0.47 AEUs per acre
0.5 < 2.0 AEUs per acre - not a CAO

## Slide 6: Example CAO Calculation #2
Dairy Farm #2
300 Milk Cows at 1,300 lbs per cow
125 Heifers at 900 lbs per cow
50 Calves at 375 lbs per cow
300 * 1,300 / 1,000 = 390 AEUs
125 * 900 / 1,000 = 112.5 AEUs
50 * 375 / 1,000 = 18.75 AEUs
390 + 112.5 + 18.75 = 521.25 AEUs Total
521.25 AEUs / 150 acres = 3.47 AEUs per acre
3.5 > 2.0 AEUs per acre - CAO

## Slide 7: CAFO – What is it?
EPA sets its rules by animal number thresholds. The Pennsylvania Department of Environmental Protection, DEP, is responsible for enforcing this program in PA. They have established the same threshold numbers as the EPA.
Operations that exceed these numbers are known as Concentrated Animal Feeding Operations – CAFOs.
CAFOs are required to apply for a CAFO permit from DEP. As part of the permitting process the farm must have a nutrient management plan developed in the same manner as a CAO.
Farm operations are also required to apply for a CAFO permit if they have more than 1,000 total AEUs or are a CAO with more than 300 AEUs.

## Slide 8: CAFO Animal Thresholds
700 Mature Dairy Cows
1,000 Total Cattle
1,000 Veal Calves
2,500 Swine, 55lbs or more
10,000 Swine, under 55lbs
500 Horses
10,000 Sheep or Lambs
55,000 Turkeys
30,000 Layers or Broilers, liquid manure
125,000 Broilers, dry manure
82,000 Layers, dry manure
5,000 Ducks, liquid manure
30,000 Ducks, dry manure

## Slide 9: Odor Management Plan
Pennsylvania’s Act 38 Law also requires all CAOs and CAFOs that are proposing new or expanded construction of an animal housing facility or manure storage to develop and implement an odor management plan.
The goal of this plan is to help select the best location on the property for the proposed structure and minimize odor impacts.
This program only regulates animal housing and manure storage, not the land application of manure.
The type of structure, number of AEUs, location, surrounding land uses (homes, public use) and township zoning all impact the odor site index score.
Scores under 50 do not require any practices, from 50 to 99 require management practices, 100 and above require level 2 practices, such as windbreaks or pit additives
This plan must be developed by a certified odor management plan writer and is reviewed and approved by the PA State Conservation Commission
The plan must be approved prior to construction starting.

## Slide 10: Ag Erosion & Sedimentation Control Plan – Ag E&S Plan
DEP requires that all farms that conduct plowing or tilling (including no-till) must develop and implement a plan that addresses soil erosion from fields and animal concentration areas.
These plans are sometimes referred to as conservation plans developed by NRCS, but must have specific items in them to meet DEP’s requirements.
They do not need to be developed by a certified plan writer and are not reviewed, but must be kept on the farm at all times.
Items that must be in a current plan include: soil loss from sheet erosion to tolerable levels, BMPs to address gulley erosion, 25% minimum field cover within 100 feet of surface water and erosion from animal concentration areas.
This plan is different then a construction E&S plan.

## Slide 11: Other Plans Related to Construction of a New Operation
Zoning
Land Development
Construction E&S / NPDES
Water Quality Permit
Manure Storage Certification
These items are typically handled by engineering staff

## Slide 12: Zoning Ordinances
Many, but not all, townships have zoning ordinances.
This document sets different zoning districts, as well as, what kinds of operations can be built within them.
They typically outline setback requirements for structures (barns or manure storages).
They can set restrictions on “Intensive Agriculture”, which is defined by the specific zoning ordinance and can be broad or specific.
If a proposed project (new CAFO) is not permitted or restricted in a zoning district, there are typically two options: conditional use permit or special exception.
Both are similar and allow the township Zoning Hearing Board to approve the project but they can place additional restrictions.
This often involves a public hearing or meeting at the township level prior to the Hearing Board issuing their decision.
This is almost always the first step in a proposed CAFO project, but some townships require a farm to develop the other plans prior to applying for a conditional use or exception.

## Slide 13: Land Development Plan
May be required by a township or county.
Depending on the specific ordinance, agriculture may or may not be exempt.
Items included in a land development plan include: property boundaries, adjoining property info, setbacks, driveway standards, lighting restrictions and storm water planning.
This plan is reviewed by the township and/or county engineer.
Review comments are forwarded to the Planning Commission where the plan will be either denied, conditionally approved or approved.
After approval by the Planning Commission the plan will be forwarded to the township supervisors for approval.
This process can include a public hearing or meeting.
Townships typically require an escrow account set up for any storm water practices that need to be implemented so that if the landowner does not install them the township can draw from the account to pay to have them installed.

## Slide 14: Construction E&S / NPDES
Construction earth moving activities require an erosion and sedimentation control plan to address sediment runoff from leaving the site.
The plan will outline practices such as: seeding / mulching, silt fence, and silt socks to control erosion.
NPDES – National Pollution Discharge Elimination System permits are required if the total earth disturbance will be over one acre.
Total disturbance includes all access driveways, site grading, storm water practices, topsoil stockpiles and the E&S controls… one acre can add up fast.
It is very hard to complete a typical poultry or swine barn under one acre.
The permit encompasses two parts: the E&S plan and a storm water management plan.
Storm water management plans outline practices to control storm water runoff from the site during and after construction.
These plans are reviewed and approved by the local county conservation district and/or DEP depending on the permit type, general or individual

## Slide 15: Water Quality Permit & Manure Storage Certification
Any livestock operation that has greater then 1,000 AEUs, has a total manure storage of 2.5 million gallons or greater, or has an earthen manure storage pond of 1 million gallons or greater that is located in an HQ/EV or agricultural impaired watershed are required to have a water quality management permit developed and approved prior to construction.
As part of this permit, DEP will review and give comments on the manure storage construction plans.
Manure storage certification is required by a licensed professional engineer for any manure storage structure built after January 29, 2000.
This includes all farms, not just CAOs or CAFOs.

## Slide 16: Example Project: QUAD Barn
Farmer is proposing to construct a 4,800 head swine finishing barn (713.42 AEUs).
The barn will have an under-building concrete manure storage that will hold 1.6 million gallons of liquid manure.
The operation will be a CAO and CAFO.
The township the farm is located in has zoning regulations that require a conditional use permit to construct a CAFO.
The township also requires a Land Development Plan that includes agricultural building construction.

## Slide 17: Planning Steps & Timeline
Farmer contacts TeamAg and provides us with details on the proposed project.
Planning and engineering staff determine planning / permitting needs and develop a proposal for the client. In this case, we determined that a conditional use hearing is required prior to construction.
After the client signs the proposal, a site visit will be completed to gather the information needed to submit the conditional use permit application.
TeamAg employees involved with the project will attend the conditional use hearing to provide expert testimony on the planning / permitting requirements of the project. This can take up to 45 days.
After the township approves the conditional use permit, the planning work can begin.

## Slide 18: Planning Steps Continued…
Now that the project has been approved by the township, a second site visit may be needed to gather information specific to each plan or permit.
The engineering staff will complete a GPS survey of the site and develop a draft site plan that includes any applicable setbacks, such as property lines or wells.
Once the client approves the draft site plan, the land development plan, construction E&S / NPDES plans and storm water management plan are prepared and submitted for review. This can take up to a month to prepare.
If a water quality management plan was required, it would be developed and submitted with these items as well.
All of these plans must be reviewed and approved prior to construction starting. This can take from 90 to 180 days from the time the plans are submitted for review.

## Slide 19: Planning Steps Continued…
The odor management plan is developed and submitted for review first as it must be approved prior to construction starting.
The nutrient management and agricultural E&S plans are developed and submitted for review and approval next.
It can take up to 90 days for the odor and nutrient plans to be approved.
Once the nutrient management plan is approved, the CAFO permit application can be submitted for review and approval. Depending on the type of permit, this will take between 45 and 145 days for review and approval.
Construction can start prior to the nutrient management plan and CAFO permits being approved, but the barn can not be populated until all plans / permits have been issued.

## Slide 20: After Construction – Now what?
After construction is complete, final storm water practices must be implemented.
The manure storage must be certified.
The odor management program must be notified prior to populating the barn.
Once manure is being generated, the farmer must keep records of: manure applications, weekly manure storage levels, any manure discharges, average AEUs.
This involves weekly, quarterly and annual reporting.
Nutrient management plans must be updated every three years.
CAFO permits and manure storage certifications must be renewed every five years.